## Slide 1: MOS Devices Literature Review
Ferroelectric Nanosheet FETs

## Slide 2
As per the Moore’s law: number of transistors on an integrated circuit doubles approximately every 2 years, leading to increase in computing power and a decrease in cost.
But as channel length went below 30 nm, Dennard scaling broke down — the power density no longer stayed constant.
Shrinking dimensions caused short-channel effects (SCEs): drain fields penetrating the channel, degrading threshold voltage () and increasing leakage.
Higher leakage leads to more static power, so new designs aim to improve electrostatics rather than just shrink size. This challenge started a geometric revolution:
Planar MOSFET->FinFET->GAA->Fe-NS FET
Each step improves gate-channel control and lowers leakage; the latest adds ferroelectric functionality for non-volatility and steep-slope switching.
Evolution of Transistor Architectures
Refs: Bohr & Young 2017 (IEEE Micro); Kim et al.,Nat. Sci. Rev. 2024 [1][3]

## Slide 3: Planar MOSFET: Strength and Limitations
The planar MOSFET uses a flat channel and a single gate on top of SiO₂. It is simple, reliable, and dominated >45 nm technology. However, its single-sided control became insufficient when . The gate potential decays into the channel with a characteristic length
Large λ → poor control → SCEs. The subthreshold slope
  is much higher than the 60 mV/dec Boltzmann limit, so leakage current increases exponentially.
DIBL often exceeds 100 mV/V. Thus, planar devices failed below 30 nm: they leaked power even when “off.”
Refs: Y. Taur & T. Ning, Fundamentals of Modern VLSI Devices (2009)

## Slide 4
To fight SCEs, Intel and other semiconductor tech giants adopted FinFETs, where a thin vertical “fin” acts as the channel and the gate wraps around three sides. This increases the effective gate area and reduces λ to roughly
Better control yields SS ≈ 70 mV/dec, DIBL ≈ 60 mV/V, and . FinFETs enabled 22–10 nm nodes and became the mainstream 3-D transistor.
Refs: Hisamoto et al., IEEE TED 2000; B. Yu et al., IEDM 2002
FinFET: First 3D solution

## Slide 5
Below 5 nm, fin-aspect limits and leakage at fin edges degrades performance due to corner-field crowding as the gate doesn’t fully surround the channel.
Tall fins complicate lithography and heat removal.
Gate-All-Around (GAA) devices fix this by wrapping the gate on all sides, giving symmetric control and uniform current.
At equal , GAA reduces DIBL by ~30 % and achieves SS ≈ 60 mV/dec – the theoretical limit for thermionic carriers.
FinFET Limits and GAA Transition
Refs: Kim et al., Nat. Sci. Rev. 2024

## Slide 6
GAA / Nanosheet FET: Concept and Structure
Motivation:
Below 5 nm, FinFETs face short-channel limits due to side-wall-only gate control.
The Gate-All-Around (GAA) design surrounds the channel completely, giving 360° electrostatic control and enabling further scaling.
Horizontal nanosheet FETs replace fins with stacked Si/SiGe sheets—each a conduction path fully wrapped by gate metal and dielectric.
Structure
3–5 stacked Si/SiGe sheets → higher drive current (Iᴅ) per footprint.
High-κ HfO₂/SiO₂ dielectric and metal gate wrap around each sheet.
Fully-depleted channel suppresses leakage and improves control.
Why it Matters
Excellent electrostatics (SCE suppression < 2 nm).
Higher Iₒₙ, lower Iₒff, CMOS-compatible process.
Basis for Fe-NS FET → adds non-volatility and sub-60 mV/dec operation.
Refs: J. P. Duarte et al., IEEE TED, 2023; S. Mukesh et al., Electronics, 2022

## Slide 7
Key Equations
Current Scaling
  → More sheets = higher drive current without larger area.
Electrostatic Integrity
  → Smaller λ (≈ 3–5 nm) → better short-channel control
Performance Snapshot
  SS ≈ 60 mV/dec DIBL < 30 mV/V 𝐼ₒₙ⁄𝐼ₒff > 10⁷
  High Iₒₙ from stacking, excellent electrostatics.
Challenges
  Complex epitaxy and selective etch
  Self-heating and strain relaxation
  Logic-only device → no data retention
Takeaway
  GAA nanosheet FETs achieve best-in-class scaling and gate control. Next step: add a ferroelectric layer to realize low-power, non-volatile Fe-Nanosheet FETs
GAA FET: Equations and Performance
Refs: J. P. Duarte et al., IEEE TED, 2023; S. Mukesh et al., Electronics, 2022

## Slide 8
Ferroelectric FET (FeFET): Concept and Physics
Concept
A FeFET replaces the gate oxide with ferroelectric Hf₀.₅Zr₀.₅O₂, storing charge via remanent polarization (±Pᵣ).
When voltage is applied, dipoles align, creating two stable polarizations ± Pᵣ. These shift the threshold voltage: logic “1” = +Pᵣ, “0” = –Pᵣ
Physics
Ferroelectric behavior follows the Landau–Devonshire model:
Negative curvature in → negative capacitance region yields NC → voltage amplification → sub-60 mV/dec switching giving voltage amplification and steep slope. FeFETs thus offer non-volatility + energy reduction.
Key Points
Advantages: Non-volatile logic, faster switching, lower VDD (~0.3–0.5 V).
Limitations: Retention loss, interface traps, weaker electrostatics in planar/FinFET.
Motivation: Combining FeFET with GAA nanosheets →
Fe-NS FET for better control and functionality.
Refs: Böscke et al., Appl. Phys. Lett. 2011; Salahuddin & Datta, Nano Lett. 2008

## Slide 9
Ferroelectric Nanosheet FET (Fe-NS FET):
The Next Step
Why Combine Ferroelectric and Nanosheet Architectures
Gate-All-Around (GAA) nanosheet FETs offer the best electrostatic control by fully surrounding the channel.
Even the GAA device cannot break the Boltzmann sub-threshold slope limit (≈ 60 mV/dec) that governs thermionic carriers.
Adding a ferroelectric layer (e.g., Hf₀.₅Zr₀.₅O₂) introduces a negative capacitance (NC) region, which amplifies gate voltage internally—producing steeper subthreshold slopes (< 60 mV/dec).
Combining both provides:
  GAA geometry→ perfect electrostatics & scalability
  Ferroelectric gate → new functionality: non-volatile polarization & voltage gain
Structure and Materials
Metal Gate: provides work-function tuning
Ferroelectric Layer: switchable polarization (± Pᵣ)
Interfacial Oxide: ensures stability & leakage suppression
Nanosheet Channel: high mobility Si/SiGe stacked layers fully enclosed by gate
Refs: P.-Y. Chen et al., Adv. Funct. Mater. 2024; Cheng et al., IEEE EDL 2025

## Slide 10
Underlying Physics
The NC effect follows a series-capacitance relation:
When , the overall increases, leading to internal voltage amplification across the channel. Landau energy:
  shows a double-well potential → two stable polarization states (± Pᵣ) usable as memory bits.
Key Benefits of Fe-NS FET
Sub-60 mV/dec switching: due to negative capacitance
Non-volatile memory: polarization remains even when power is off
Ultra-low VDD (0.3–0.5 V): ≈ 40–60 % dynamic-power reduction
Uniform electrostatics: each nanosheet fully gated → minimal leakage
Scalable below 2 nm: ferroelectric HfZrO₂ films ~10 nm compatible with CMOS processes
Reconfigurability: switching P state modulates Vₜ → useful for logic-in-memory and neuromorphic hardware
System-Level Impact
Fe-NS FET bridges logic and memory in one device—reducing data movement energy in CPUs and accelerators. It enables non-volatile, low-power systems for AI edge devices and IoT nodes. With optimized interface engineering and HfZrO₂ thickness control, prototypes demonstrate >10⁸ cycles endurance and multi-bit operation
Refs: P.-Y. Chen et al., Adv. Funct. Mater. 2024; Cheng et al., IEEE EDL 2025

## Slide 11
Electrostatics: Full gate + negative capacitance → superior control even at < 2 nm. Energy: Sub-Boltzmann SS enables ultra-low-voltage logic. Functionality: Non-volatile, logic-in-memory, reconfigurable . System-level gains: Less data transfer between logic & memory → lower delay and power; ideal for neuromorphic/edge AI. Typical metrics: , , >10⁸ cycles endurance, >10 years retention.
Evolution path:
Planar MOSFET: simple but leaky.
FinFET: 3-D geometry → better control.
GAA: full gate wrap → near-ideal electrostatics.
Fe-NS FET: adds ferroelectric gate → non-volatile & ultra-efficient. Why the combination: GAA handles electrostatics, ferroelectric supplies new physical functionality — together achieving both performance and memory in one device. Future focus: ferroelectric reliability (fatigue, retention), interface traps, thermal control in stacked sheets. Vision: “Logic + Memory in one transistor” — a building block for beyond-CMOS and neuromorphic systems.
Refs: Hoffmann et al., AIP Adv. 2020; Chen APR 2022; Adv. Funct. Mater. 2024
Advantages and Applications of Fe-NS FETs

## Slide 12
D. Hisamoto, W.-C. Lee, J. Kedzierski, H. Takeuchi, K. Asano, C. Kuo, E. Anderson, T.-J. King, J. Bokor, and C. Hu, “FinFET—A Self-Aligned Double-Gate MOSFET Scalable to 20 nm,” IEEE Trans. Electron Devices, vol. 47, no. 12, pp. 2320–2325, Dec. 2000. doi:10.1109/16.887014. SCIRP+1
B. Yu, L. Chang, S. Ahmed, H. Wang, S. Bell, C.-Y. Yang, C. Tabery, C. Ho, Q. Xiang, T.-J. King, and C. Hu, “FinFET Scaling to 10 nm Gate Length,” IEDM Tech. Dig., 2002, pp. 251–254. doi:10.1109/IEDM.2002.1175825. ResearchGate+2Semantic Scholar+2
Q. Zhang, Y. Zhang, Y. Luo, H. Yin, et al., “New structure transistors for advanced technology node CMOS ICs,” National Science Review, vol. 11, no. 3, article nwae008, 2024. doi:10.1093/nsr/nwae008. OUP Academic+2PubMed+2
S. Mukesh and J. Zhang, “A Review of the Gate-All-Around Nanosheet FET Process Opportunities,” Electronics, vol. 11, no. 21, 3589, 2022. doi:10.3390/electronics11213589. MDPI
S. Salahuddin and S. Datta, “Use of Negative Capacitance to Provide Voltage Amplification for Low Power Nanoscale Devices,” Nano Letters, vol. 8, no. 2, pp. 405–410, 2008. doi:10.1021/nl071804g. American Chemical Society+2PubMed+2
T. S. Böscke, J. Müller, D. Bräuhaus, U. Schröder, and U. Böttger, “Ferroelectricity in hafnium oxide thin films,” Applied Physics Letters, vol. 99, 102903, 2011. doi:10.1063/1.3634052. AIP Publishing+1
H. Chen, H. Liu, H. Zhang, et al., “HfO₂-based ferroelectrics: From enhancing performance, material design to applications,” Applied Physics Reviews, vol. 9, 011307, 2022. doi:10.1063/5.0066607. AIP Publishing+1
J.-Y. Kim, J.-H. Lee, H.-S. Kim, and J.-P. Hong, “Ferroelectric field-effect transistors: Progress and perspective,” APL Materials, vol. 9, 021102, 2021. doi:10.1063/5.0039636. AIP Publishing
Y. Yang, Z.-D. Luo, X. Wang, et al., “Emerging Opportunities for Ferroelectric Field-Effect Transistors: Integration of 2D Materials,” Advanced Functional Materials, vol. 34, no. 21, 2024, 230?—Article ID 2310438. doi:10.1002/adfm.202310438. Astrophysics Data System
H. Wong and K. Kakushima, “On the Vertically Stacked Gate-All-Around Nanosheet and Nanowire Transistor Scaling beyond the 5 nm Technology Node,” Nanomaterials, vol. 12, 1739, 2022 (open-access tutorial/analysis). PMC
Y. Zhao, S. Wang, J. Xiong, et al., “Compact Modeling of Advanced Gate-All-Around Nanosheet FETs Enabled by Artificial Neural Networks,” Micromachines, vol. 15, no. 2, 218, 2024. MDPI
References

## Slide 13: THE END